## Slide 1: Fundamentals of Electric Aircraft/eVTOL Design
Tony Tao
2022.09.13
16.82x

## Slide 2: Electric Flight
Question 1:
How do we design electric aircraft?
Question 2:
Why do eVTOLs look so weird?
What drives these designs?
Lecture Sections:
Powertrains
Electric Range
eVTOL Configuration

## Slide 3: 1. Powertrain Elements

## Slide 4: (Fuel & engines) vs (Batteries & motors)
ICVs tolerate engines to use fuel.
EVs tolerate batteries to use motors.
Performance
Complexity & Cost
Power
Energy
Power
Energy

## Slide 5: How do batteries work?
Load (ESCs, motors, etc)
Anode
terminal (-)
Cathode
terminal (+)
Li+
Separator
Cathode
Anode
e-
Goo (organic solvent electrolyte)
Load (ESCs, motors, etc)
e-
“Current” (amps)

## Slide 6: What’s actually depleting in a battery?
Load (ESCs, motors, etc)
Li+
Separator
Cathode
Anode
e-
Load (ESCs, motors, etc)
Li+
Separator
Cathode
Anode
e-
Full battery
Empty battery

## Slide 7: Voltage, Current, C-rate, Power
100% SoC
0% SoC
100% SoC
0% SoC
2C
6C
Thing | Units | Variable | Think…
Mass | Kg |  | Obvious
Voltage | Volts |  | Electrical pressure
Current | Amps |  | Electron flow rate
Capacity | Amp*hours |  | Max electron capacity
C-rate | 1/hr |  | How hard you’re pushing the batteries
Power | Watts |  | Rate of work
State of charge | - |  | Percent of electrons in reserve
Thing | Units | Variable | Think…
Mass | Kg |  | Obvious
Voltage | Volts |  | Electrical pressure
Current | Amps |  | Electron flow rate
Capacity | Amp*hours |  | Max electron capacity
C-rate | 1/hr |  | How hard you’re pushing the batteries
Power | Watts |  | Rate of work
State of charge | - |  | Percent of electrons in reserve
Power:
Current:
Voltage:

## Slide 8: Battery Weakening with C rate
Emptying in 3 mins
Emptying in 60 mins
Emptying in 3 mins
Emptying in 60 mins
Brian J. German, “Introduction to Batteries and Cell Discharge Modeling for Electric Aircraft Design” AIAA Aviation, Atlanta, Georgia, June 2018
Power:
Current:
Voltage:

## Slide 9: Battery Goodness
Goodness
Hover or Acceleration
Cruise range
Metrics of goodness:
Specific ENERGY
Specific POWER
Other considerations:
Internal resistance
Cost
Cycle degradation rate
Cooling, cooling, cooling!
Whoever is in charge of the batteries, watch this video:
https://www.youtube.com/watch?v=QlDd3jkcxoQ
Trade off

## Slide 10: Electric Motors
Example commutation
0-th order mental model:
is a function of the winding count.
The ESC feeds forward effective based on (auto)pilot input.
Motor will “pull” current, up to its maximum torque or power (whichever is limiting) to achieve this RPM. Inefficiency is lost as heat.
Start thinking of motors in terms of RPM, Torque
Example efficiency map

## Slide 11: Internal Combustion Drivetrains
Specific Energy | ~46 MJ/kg | 
Specific Power |  | ~1000 W/kg
Specific Torque |  | ~1 ~2 Nm/kg
Efficiency |  | 0.2 ~ 0.3
Moving Parts | 0 | lots
Thermals | -45°C ~ 250°C | ~ 800°C
Specific Energy | ~46 MJ/kg | 
Specific Power |  | ~1000 W/kg
Specific Torque |  | ~1 ~2 Nm/kg
Efficiency |  | 0.2 ~ 0.3
Moving Parts | 0 | lots
Thermals | -45°C ~ 250°C | ~ 800°C
Fuel
Engine Block
Support Equipment
Carburetor(s)
Engine Control Unit
Alternator
Airbox & Air Filter
Exhaust/ Muffler
Engine System
Prop
(Typical values)

## Slide 12: Electric Drivetrains
Batteries
Electronic Speed Controller (“ESC”)
“Motor Driver”
Motor
Specific Energy | Cell-level ~180 ~240 Whr/kg |  | 
 | Pack-level ~130 ~180 Whr/kg ~0.5-0.7 MJ/kg |  | 
Specific Power | Energy-biased: ~500 W/kg Power-biased: ~2000 W/kg | ~20,000 W/kg | ~5000 W/kg (big motors) ~10,000 W/kg (small motors)
Specific Torque |  |  | ~10 Nm/kg
Efficiency | Function of Cr, ~93% over a mission | >~0.95 above 50% throttle | ~0.90 ~0.95
Moving Parts |  |  | 1
Thermals | 10°C - 60°C (longevity) …. 100°C (combustion) | ~80°C | ~100°C
(Typical values)
Prop

## Slide 13: 2. Electric Aircraft Range

## Slide 14: Breguet Range Equation
Gravity
Aerodynamics
Total fuel burned
Propulsive Efficiency
Energy density of fuel
Cessna 172
Range: 696 mi

## Slide 15: Electric Range Equation
Gravity
Aerodynamics
Battery mass ratio
Propulsive Efficiency
Battery chemistry
Multi-rotors: ~1
Fancy helicopters: ~3-6?
Winged vehicles: 10+
(This is why we need wings.)
Pipistrel Alpha Electro
86 miles advertised

## Slide 16: 2. eVTOL Configuration

## Slide 17: Futurama said it best

## Slide 18: Configuration Flexibility Provided by Electric Drivetrains
Cost per propulsion unit | $$$$ | $
Single propulsion unit loss |  | 
Airflow shaping | O | ooOOOooOOooo
Controllability | Few, slow | Many, nearly instant

## Slide 19: The eVTOL Design Space
Propulsion Tilt
0%, cruise on wing
100%
(typically 33% to 50%)
“Big multicopter”
“Separate Lift Cruise” (SLC)
“Tilt something”
“Tilt everything”
Volocopter
CityAirbus
eHang
Embraer Eve
Boeing PAV
Wisk
Archer
Hyundai
Heaviside
Joby S4
Lilium Jet
Winged
Hover only

## Slide 20: Typical VTOL Mission Power Profile
Hover Takeoff
(HTO)
Outbound Transition (OT)
Inbound Transition (IT)
Hover-land
(HL)
Cruise
Hover and outbound transition are usually driving from configuration standpoint
Inbound transition and Hover-land are usually configurationally easy if HTO, OT are met, but must be accomplished with reduced max power
Cruise: Electric range equation, as previously discussed

## Slide 21: Hovering Power
“Ideal Hover Power”:
(Power delivered uniformly into air molecules)
w
w
w
Power: 100%
~90%
~70%
Assuming you get to choose the best-possible propeller in each situation, you want to minimize disk loading (Thrust over Area).

## Slide 22: Big Multicopters
Minimize disk loading + Maximize battery fraction = Works fine
No transition required; just hover around
Top speed 30~50 mph
Short range (10-20 miles?)
Limiting factor for forward flight: trade hover efficiency for forward speed, rotor vibe
Volocopter
chAIR
https://youtu.be/GKBNTP6D1ag?t=563

## Slide 23: A word on RPM Thrust Control
Thrust:
Torque:
Power:
Thrust slew rate (N/s)
(rad/sec)
(Nm)
Propeller inertia
Max rotor speed
Magnetic shear limit
Power limit
Bearing limit
Thrust and torque coeffs
Notes: By the way, there is no commonly accepted name for .
It has the units of , or mass*jerk. I’ve been thinking of calling it the Elon because he is a massive jerk.
By the way, there is no commonly accepted name for 𝑁/𝑠.
It has the units of 𝑘𝑔 𝑚/𝑠^3 , or mass*jerk. I’ve been thinking of calling it the Elon because he is a massive jerk.

## Slide 24: Hover Power and Disk Loading
High disk loading
High P/W for hover
High pitch speed, can go fast
Low disk loading
Low power needed to hover
Low pitch speed, can’t go fast

## Slide 25: Hover and Winged Balance
Multirotor – CG centered between rotors
Add wing – large CG mismatch between rotors and winged neutral point
Shift rotors, add tail
NP
NP
W
MR
For easy stability, mean aero area wants to be behind the mean rotor area

## Slide 26: The Forward Transition Problem: 1: Pitching moment
Vehicle motion convects clean air to front rotors
Tailward rotors operate in the wake of forward rotors
Tailward rotors must spin faster and exert more power ( effect)
Combined wake impinges on the tail, (nose up moment)
Trying to correct this force using tailward lift rotors increases the wake on the tail… see #4.
Hover
Forward motion

## Slide 27: Lateral vs Longitudinal Rotors
(+) Better rotor performance in transition
(-) More boom drag
(-) Downwash stacking in transition
(+) Reduced boom drag

## Slide 28: The Forward Transition Problem: 2: Pitch schedule
Nose up for more wing lift
Nose down for more rotor thrust
Essentially, the wing and the propellers are out of phase in what they want.

## Slide 29: An Efficient Option: Reallocating Forward Power to Acceleration

## Slide 30: The Other Problem…Rotors in Edgewise Flow
Lift center (V=0)
Velocity
RPM
0
Vehicle stall speed
Lift center (high V)
First flapping mode
(Graph is notional; data for RPM schedules are typically highly proprietary)

## Slide 31: Variable Pitch and Tilt
Hover
Climb
Cruise
Velocity
RPM
0
Vehicle stall speed
First flapping mode
Variable pitch allows keeping RPM constant, keeping out of vibrational modes
SLC

## Slide 32: Joby S4 – “embrace complexity” posterchild
6 rotors, 5 blades each
6 variable pitch mechanisms
6 tilt mechanisms
12 aero control surfaces
Total of 30 control channels (by my count)
~2000 kg all-up
200 mph

## Slide 33: Oddballs (or why innovation isn’t over yet)
PteroDyanmics Transwing
  https://youtu.be/rjX-vd2Zln0
  https://youtu.be/7LNeVcziDus?t=893
PAL-V Tilting Trike/Autogyro
https://youtu.be/CajAq6ndJYE?t=96
(Think duck-billed platypus of air vehicles)

## Slide 34: Electric Short Takeoff and Landing (eSTOL)
What if we invested all this acceleration horizontally instead of vertically?
Blown lift allows wings to generate much higher lift than otherwise (up to ~5x)
Airframe is nearly conventional, and propulsors are much simpler
eSTOL
eVTOL SLC
Takeoff geometry, roughly to-scale
Initial demonstrator

## Slide 35: A note on hybridization
Structures
Motors
Avionics
Batteries
Engine/Generator
Fuel
Payload
1
Range
Structures
Motors
Avionics
Batteries
Payload
Range
1
Specific energy of fuel, L/D of a hybrid airframe
Specific energy of batteries, L/D of electric airframe
Minimum battery to provide hover power
Compared with pure-electric vehicles, hybrid vehicles want more power-focused batteries
All-electric
Hybrid
0
0
Best
possible
payload envelope

## Slide 36: Commentary
Venture $
Question | Answer
Are manned eVTOLs viable technically? | Absolutely - but high performance configurations aren’t simple.
Are manned eVTOLs viable economically? | Most of them, probably not. Time will tell for the better ones.
Why do they look so different? | 1. Some designers are still quite naïve, and money was loose. 2. Some designers are hunting for the knee of the complexity/performance curve. 3. Venture capital is attracted to new, wacky designs.
What’s the biggest hinderance to them being operational? | Toss-up between battery energy, battery thermals, economics, and the FAA.
Is all-electric or hybrid better? | Depends on the range required. Battery chemistry matters.