## Slide 1: Persistent Solar Powered Airplanes: Closing the Energy Cycle
Dr. Kevin R. Uleck
11 February 2020
Uleck.kevin@aurora.aero

## Slide 2: Kevin R. Uleck, PhD Program Manager, Odysseus Solar UAV, Aurora Flight Sciences
UAV Experience:
Concept Study through Program of Record
  Aurora Flight Sciences (Since 2002)
    Perseus-B
    CUAV / GoldenEye-100
    GoldenEye-50
    OAV-II / GoldenEye-80
    Excalibur
    Vulture:
    RapidEye
    High altitude airship (LM sub)
    Solar UAV (PM, present)
  Raytheon
    KillerBee
  AAI / Textron
    Shadow 200 (RQ-7B)
    Shadow M2
    Aerosonde
Education:
  BS, MS, PhD @ U. Maryland
    Composite structures
    Aerodynamics, helicopters
    UAV lab co-founder
Outside the office:
  Musician – lots of performing
  Runner, cyclist
  Dad to 3 great kids!

## Slide 3: Solar Airplane Energy Challenge: Closing The Energy Cycle
Energy In
  Solar flux in space
  Atmospheric absorption
  Shape / Collection factor
  Length of day vs DOY, latitude
  Solar panel efficiency
≥ Energy Required
  Flight Energy = Power * Time = Thrust*Velocity * 24 hours
  Energy storage: needed to last though the night
  Flight Speed > wind speed
  Thrust = Weight/(L/D)

## Slide 4: Closing The Energy Cycle
Two Conditions must be met:
Energy In ≥ Energy Used over 24 hour cycle
Battery Energy ≥ Energy Required for “Night”
Two primary solar power flows:
  Daytime flight power
  Energy storage for nighttime flight

## Slide 5: Energy In: Solar Power Available
Usable Power = Flux in Space *Area of Solar Array * (ηAtmosphere*ηCollectionFactor*ηConversion)
Solar flux in space ~ 1367 W/m2 (standard nominal value)

## Slide 6: Energy In: Latitude & Length of Day
Hours of sunlight function of day of year, latitude, altitude
Hours of Darkness drives how much battery is required
Notes: In winter months (autumnal equinox to vernal equinox), flying south increases daylight. However, in summer months (vernal equinox to autumnal equinox), moving North increases daylight. A key takeaway is that airplane must be able to fly at least 11 hours on battery else it is a summer only airplane and might not even be able to cover equatorial regions!

## Slide 7: Energy In: Solar Power Available- Atmospheric Absorption
Solar flux absorbed by atmosphere
Absorption depends on mass and composition of air through which sunlight travels
  Common reference conditions referred to as AM1.5 (sea level standard) and AM0 (space)
  Flux available f(altitude, solar angle)
Spectral content also changes as light is filtered through atmosphere – impacts solar cell efficiency
  Solar cell efficiency typically reported for AM1.5 conditions
Notes: Check Alta cell spectral efficiency

## Slide 8: Energy In: Solar-Electric Conversion Efficiency
Solar cell spectral efficiency determined by junction materials, packaging, number of junctions
  Single junction installed ηmax≈24% for GaAs or Si
Maximum efficiency of single junction cell limited to ~34% (the Shockley-Queisser limit)
Multiple junction cells use larger bandwidth of available solar flux to achieve higher efficiency
Alta GaAs cell
Spectrolab 3J cell

## Slide 9
What we are using

## Slide 10: From cell efficiency to useable power
Final installed solar conversion efficiency is affected by many factors

## Slide 11: Energy In: Solar Panel Area
Power collected is proportional to solar array size, more array = more energy!?
Factors to consider for aircraft application of solar array
  Power/Weight: different solar cell technologies offer range of weight / area for different price, efficiency, and durability
  Area available: wings and surfaces might need to be increased beyond aerodynamically required size
  Orientation: Aerodynamically shaped surfaces offer different compromises to sun tracking  collection factor
  Flexibility  Durability and formability
SolarImpulse
Helios

## Slide 12: Energy In: Incident Flux Collection Factor
Angle between sun vector and solar panel surface normal determines incident power (cosine losses)
  Sun vector normal to panel  100% power
  Sun vector parallel to panel  0% power
Additional losses at low solar incidence angles due to surface reflection
Angle depends on sun elevation, and aircraft attitude
  Changes throughout the day and with vehicle heading

## Slide 13: Energy In: Collection Factor (2)
Aircraft geometry affects relative solar incidence angle, and surface shadowing
Notes: Look at variation of solar power over wing chord!

## Slide 14: Energy In: Solar Cell Power Point Tracking
Solar cell can be operated at any voltage from full short up to junction voltage (VOC)
Power output is product of current * voltage
Circuit voltage regulation required to operate solar cell at peak power point to obtain maximum output
  Typically achieved through Maximum Peak Power Point trackers, essentially DC-DC converters setting circuit voltage
Achieving maximum efficiency requires dynamic matching of load to solar array output

## Slide 15: Energy Required: Daily Energy Breakdown
Question to answer: How much energy is needed to fly for 24 hours?
  Majority of energy goes to propulsion
  Propulsion Energy = Power * Time = Thrust*Velocity * 24 hours

## Slide 16: Propulsion Power Required = Thrust X Airspeed
For steady level flight, Thrust = Drag
Drag = Weight/(L/D)
  L/D = Lift-to-Drag ratio, measure of aerodynamic efficiency.
    Determined by aerodynamic profile and operating condition
    Minimum power airspeed
  Drag is proportional to Weight
  Drag is proportional to Airspeed2
Thrust Power = Thrust * Airspeed
  Power required is proportional to airspeed cubed
  To minimize power required, fly slow!
Chart: Thrust Power, 67.5kft
| 0.6 | 0.7 | 0.79999999999999993 | 0.89999999999999991 | 0.99999999999999989 | 1.0999999999999999 | 1.2 | 1.3 | 1.4000000000000001
Power (W) | 7160.0423 | 6138.4903 | 5453.2142 | 5016.6306 | 4738.4494 | 4608.1937 | 4661.8953 | 4926.5761 | 4840.1906
Op Point
Odysseus cruises on 6.5 hp!

## Slide 17: How slow can we fly? Must stay on station against winds!
99th Percentile wind speeds (m/s) at 50 mbar pressure level (approximately 67,500 ft)
Data Source: NOAA NCEP/NCAR Reanalysis 1

## Slide 18: Energy Required: Night and Day
Two power system modes:
Daytime: Solar array power > required power
  Array power  propulsion motors, avionics, & charge battery
Nighttime: All required power from onboard batteries
  Required battery capacity = Power required * length of night
    Sets required battery size & mass
  Typical battery energy storage density ranges from 50 Wh/kg for lead-acid to 400 Wh/kg for emerging technology lithium battery types
    Gasoline and diesel ~4,000 Wh/kg usable (12,000 Wh/kg X 33% η) >10x the best batteries available today!!
  Battery energy storage has loss – energy recovered ~90-95% of energy input
  Must account for battery packaging, typically 15-25% of cell mass

## Slide 19: Mass
Wing loading ~1 psf  very light structures & systems!
Energy storage accounts for 42% total mass in Odysseus. Location and distribution of this mass drives structure
3.8% payload fraction!
Ultra-Lightweight Structures & Components!!
Odysseus baseline mass distribution
Aurora proprietary information – not for distribution
Everything must be lightweight!
From Ref 1

## Slide 20: Energy Balance- Example
Climb-and-glide energy storage

## Slide 21: Energy Cycle: Putting it together
Key mission parameters: Latitude and Day of Year
  Sun angle & length of night both function of latitude and DOY
  Drives energy available and energy storage requirement
Key Aircraft parameters: Weight, L/D, Flight speed
  Drives energy needed
Day | Hours of Night | E Collected (kWh) | E Storage Required (kWh)
Winter Solstice | 14.2 | 154 | 85
Equinox | 11.8 | 191 | 70
Summer Solstice | 9.5 | 227 | 57
Latitude: 35 deg N, Altitude: 65,000 ft, Odysseus Baseline
50% more battery required to make it through winter night

## Slide 22: Solar Airplane Optimization and Sizing Keys
Optimization Objective: Minimize size & cost of solar powered airplane for a given set of technology inputs; or determine technology required to achieve a given mission
Key Sizing Drivers:
Mission definition: latitude, time-of-year, min flight speed
Key technology and its parameters: power collection system, energy storage system, fixed mass components (avionics)
Sizing scaling: nearly everything scales!
  Energy storage system: scales with energy stored
  Structural sizing: scales with loads, mass (& its distribution), airspeed, aeroelastic effects
  Power distribution and wiring: scale with power, length, efficiency
  Electric motors: scale with torque, efficiency
  Servo actuators: scale with control surface size, airspeed
  Landing gear: scales with height, gross mass, speed
  …

## Slide 26: References
https://www.researchgate.net/publication/228843407_Fly_Around_the_World_with_a_Solar_Powered_Airplane
https://www.researchgate.net/publication/336455359_Review_of_Power_Device_for_Solar-Powered_Aircraft_Applications
https://engineering.fb.com/connectivity/open-sourcing-facebooks-solar-powered-aircraft-design-tools/
https://research.fb.com/publications/hale-multidisciplinary-design-optimization-part-i-solar-powered-single-and-multiple-boom-aircraft/
https://research.fb.com/publications/hale-multidisciplinary-design-optimization-part-ii-solar-powered-flying-wing-aircraft/
https://arc.aiaa.org/doi/10.2514/1.C034405

## Slide 27
Thank you!
Questions?